## Slide 1
A1.1.1 Update on Review of beam parameters in FLASH radiotherapy
1. Beam parameters of LINAC systems
100 – 300 Gy/s, 0.5 – 11 Gy/pulse, 100 – 300 Hz
Studies seem to converge on the main role of Total irradiation time  may imply the use the high frequency range (200 – 300 Hz) for lowest DPP systems.
Ruan et al. 2021: Intestinal crypt survival (non-significant on toxicity)
  Increasing the total time diminished/impaired the Flash benefice (3.4 µs >> 10 – 290 ms >> more).
  Increasing the time interval between pulses > 40 ms impaired the Flash benefice with/without increasing total time.
  Shorter time interval (10 ms) can be better than higher dose/pulse (5.6 vs 2.2 Gy/p) or even than shorter time (40 ms vs 290 ms).
2. Beam parameters of clinical proton beams:
60 – 125 Gy/s, ns-pulses, 1 or more macro-pulse(s)
Duty cycle
Quasi-continuous proton beams (= isochronous cyclotrons Varian ProBeam, IBA Proteus PLUS) :
  Duty cycle ~ 15-20%, Pulse Length 1 – 3 ns, 70 – 100 MHz frequency, Macro-pulse Length = Irradiation time ~ 100 ms
  FLASH effect demonstrated in Mouse intestine, skin, muscle, bone
Synchro-cyclotron (Mevion HYPERSCAN, IBA Proteus ONE): the extracted beam has macro-pulses
  Duty cycle ~ 0.05% - 1.5%, Macro-pulse length ~ µs – ms, Macro-pulse frequency ~ 25 – 650 Hz
Karsch et al. 2022: FLASH effect demonstrated in Zebrafish development
  Single-pulse (300 µs) vs Continuous vs Macro-pulse structure (Average dose-rate equal, DPP x 1000)
  Increasing the total time diminished/impaired the Flash benefice (300 µs >> 168 ms).
  No difference between Quasi-continuous and SynchroCyclotron time structure.
Darafsheh, Medical Physics Letters, 2020
3. X-rays systems
ESRF synchrotron
  37 Gy/s, 10 Gy/pulse, Quasi-continuous beam (bunch length ~ ps, bunch repetition frequency ~ MHz)
  FLASH effect demonstrated in Mouse brain
PARTNER @Chengdu THz Free Electron Laser facility:
  700 – 1200 Gy/s, 10 – 30 Gy/pulse, Quasi-continuous beam
  FLASH effect demonstrated in Mouse lung, intestine